http://www.f150forum.com/showthread.php?t=16265

24 pin
Green/purple - radio 12 volts
black/lt green - radio ground
black - ground
pink/black or pink/yellow - radio ignition (12 volts when key is on)
blue/red - radio illumination
green/purple - factory amp (12 volts)
grey/black - speed sensor (increase/decrease volume)
orange/lt green - left front speaker +
blue/white - left front speaker -
white/lt green - right front speaker +
dark green/orange - right front speaker -
grey/lt blue - left rear speaker +
tan/yellow - left rear speaker -
orange/red - right rear speaker +
brown/pink - right rear speaker -

16 pin (audiophile for rear stock woofer)
Dark green/violet - sub amp enable
black/orange - ground
violet/lt blue - voltage supply at all times
brown/orange - sub woofer signal +
red/black - sub woofer signal -
black - shield