Auto Spring Kits

2009-2010 Expedition and 2009-2010 F-150 Front Coil/Strut

1-1/2" Lift Kit or 2" Lift Kit or 2 ½" Lift Kit

Installation Instructions

15, 17mm wrench & deep socket	1	Tech Support contact: 1-800-345-0431

30mm socket or 1-1/16" socket              1                                  www.autospringcorp.com

1-1/16" wrench				1	                        PATENT PENDING

17, 18 & 21 mm deep sockets		1		          Fax:208-362-6310

Small bottle jack		 	1                           address:8007 W. Mossy Cup st.

Floor Jack				1		        Boise, Idaho 83709

Jack Stands                                          2

1 or 2 lb. Hammer			1

Installation Instructions:

1.	Before beginning, read instructions completely.

2.	Jack up one side of vehicle as per manufacturer recommendation and support with jack stands on the frame.  Lift front enough to raise the front tire off the ground.

3.	Remove the front tire using a 21mm socket.

4.	Disconnect the lower sway bar link attached to the lower control arms using a 18mm deep socket.

5.	Remove the large lower strut assembly bolt using a 30mm socket on the nut and a 1-1/16" wrench on the bolt head.  NOTE: an impact wrench will be helpful to remove this bolt.  It is very, very tight.

6.	Remove three upper strut nuts on the strut tower using a 15mm socket and wrench.  Remove the upper ball joint nut with a 21mm socket or wrench.  Strike the steel spindle near the upper ball joint with a sledge hammer.  The sharp vibration will cause the ball joint to pop loose from the spindle and allow the lower control arm to swing down allowing the removal of the strut assembly.  Now, lower the strut assembly down from the upper strut tower.  Remove the strut assembly from the vehicle.  You should now be able to access the upper strut plate.  (Top of strut)

7.	Install the marked spacer either drivers side or passengers side on top of the strut. The holes will only line up one way and use the factory nuts and a 15mm wrench to bolt the spacer to the strut.  Torque the three nuts to 25 ft lbs. MAKE SURE THE DRIVERS SIDE SPACER IS ON THE DRIVERS SIDE STRUT.

8.	Re-install the strut back in the upper strut tower and start nuts on the three studs that extend thru the tower.  Use the nylock nuts provided in the kit. Just slightly tighten the nylock nuts with a 17mm wrench. Torque to 35 fts after the lower strut bolt is installed.

9.	Place the small bottle jack between the lower control arm and a solid spot on the upper strut tower.Extend the jack enough to allow the lower strut mount to drop back into its mounting pocket. This allows re-install of the lower strut mount in the lower control arm. Re-install the lower strut bolt.  Torque to 200 ft. lbs.

10.	Jack up the lower control arm and connect the upper control arm to the spindle.

11.	Torque the upper ball joint nut to 90 ft. lbs.

12.	Reconnect the lower sway bar end links.  Torque to 35 ft. lbs.

13.	Install the front tire and torque lug nuts to factory specs.

14.	Carefully lower the vehicle to the ground and torque lug nuts to factory specs. Repeat the strut removal process and spacer installation on the other side of the vehicle.

15.	ALIGN THE VEHICLE.  Re-aligning the vehicle must be done to allow the suspension to relax to its proper ride height (the tires will be toed-in which will cause severe tire wear and will force the front to sit too high).  Re-aligning the vehicle is required with any lift/leveling kit.  Re-torque all bolts after 300 miles.

WARNING!  Installation of this kit should be by a certified or competent mechanic only.  Adjust headlights after installation.